## Slide 1: Air Systems Modelling and Simulation
Model & Sizing of Aircraft Air-Conditioning Systems – 2023

## Slide 2: Agenda
          Air Systems functions
          System modelisation
          Dymola overview
          Dymola exercise
          System modelisation at Liebherr Toulouse
          Future of system simulation
          Fluid Modelling and Humidity effect
          Flow schedule Usecase & exercise

## Slide 3
Air Systems

## Slide 4: Main Aircraft Operational Functions
Air Systems
Ensure A/C Integrity
Maintain Humans Alive
Offer Air Conditioning
Offer Comfortable Travel
Protect from Hypothermia
Protect from Hyperthermia
Maintain Metabolic Functions (O2)
Air Systems
Transport Passengers
Limit Mechanical Loads

## Slide 5: Distribution and Cabin Pressurization Systems
Air Systems
DS & CPCS
Adapt Zone Air Temperature
Distribute Air over Zones
Recirculate Zone Air
Protect Aircraft From Pressure Loads
Provide Adapted Pressure for Human
Air Conditionning Packs
Passengers Air Distribution Ducts
Acronym
DS : Distribution System
CPCS : Cabin Pressurization Control System
Recirculation Fans
Pilots Air Distribution Ducts

## Slide 6: Environmental Control System
Air Systems
ECS
Provide enough fresh air
Provide Cold Air
Provide Hot Air
Reduce Humidity level
ECS Integration
„Classical“ ECS Architecture
Acronym
ECS : Environmental Control System

## Slide 7: Bleed Air System
BAS
Maintain Consumers in Operation
Protect Consumers from Engine
Select Power Source
Protect Aircraft from Hazard
Air Systems
Acronym
BAS : Bleed Air System
EBAS : Engine Bleed Air System
Air Sources
Air Consumers
„Classical“ EBAS Architecture
EBAS Integration

## Slide 8: Architecture Synthesis
Air Systems
BAS
ECS
DS
CABIN
WIPS
APS
ENG
APU
HPGC
CPCS
Ambient
Air
Ambient
Air
Ambient
Air
Ambient
Air
Ambient
Air
Conventional Aircraft Air Systems Architecture

## Slide 9: System Type
Air Systems
Computer
Physical Hardware
Sensors
Commands
Air Systems:
Cyber-Physical Systems
Configuration

## Slide 10
System Simulation

## Slide 11: What is a System ?
System Simulation
Modulate Permeability
Exchange Heat
Modulate Electrical Resistance w. Temperature
Acquire Sensors
Compute Commands
Command Actuators
Main Equipment Function(s)
Pneumatic Valve
Heat Exchanger
Temperature Sensor
Computer
///
Assembly of “sub-elements” with more simple functions : Complexity Management

## Slide 12: What is a System ?
System Simulation
///
Emergence of System function(s) thanks to the chosen Architecture : High Level Services
Control Temperature
Temperature Regulation
Air Preparation System Architecture
Properties
Temperature Regulation Performances
Temperature Limitations
Failures Modes
Monitoring
Reconfiguration
…
System Architecture is results of design choices !
Pneumatic Valve
Heat Exchanger
Temperature Sensor
Computer

## Slide 13: What is Simulation ?
System Simulation
///
Simulation is a support for Analysis
Requirements
Solution
Needs Analysis
Architecture Principles
Design Activity
Design Choices
Need Elicitation
Design Feedback & Validation
Design Questions
Analysis Activity
Analysis Results
Simulation
Test Benches
Theory
Engineering Assessment

## Slide 14: What is Simulation ?
System Simulation
///
Simulation Requires a large set of information as input
Simulation
Model
Multi-physical equations
Control Equations
Events Modelling
Safety,…
Solver
Robustness, Accuracy, Computational Cost
Results
Produced data (unknowns,…)
Requirements to Validate / Verify
Parameters
Test Scenarii
Properties
Definition

## Slide 15: What is “System Simulation” ?
System Simulation
///
Performance Example
Computer
Physical Hardware
Sensors
Commands
Configuration
Functions
Interfaces
System Performances
Mechanics
Electrical
Pneumatic
Control
Thermal
Architecture
Hydraulic
Physical Domains
Equip. Performances
System Definition
Modeling of
Cyber-Physical Systems

## Slide 16
Dymola (Short) Overview

## Slide 17: MODELICA & DYMOLA Overview
Dymola (Short) Overview
MODELICA
Ex : Simulink, …
Mathematical bloc modeling (causal)
Ex : Modelica, SimScape, …
Organic modeling (acausal)
System of Interest
Define the mathematical problem including simplifications (by hand) and causality (boundaries)
Implement the mathematical problem by avoiding algebraic loops
Define the physical equations of each components
Implement the physical equations
The MODELICA interpreter will perform the final implementation by simplifying and determining the causality itself

## Slide 18: MODELICA & DYMOLA Overview
Dymola (Short) Overview
Interface
Organic Modeling
Component
Environment
Interface
Connection
Connectors: Definition of exchanged variables (depending on physical domains)
Interface: Set of connectors (potentially using several physical domains)
Component: Relations between connectors variables
MODELICA

## Slide 19: MODELICA & DYMOLA Overview
Dymola (Short) Overview
Connector
Interface
Component
Comp1
Comp2
Connection
Generate
Definition of exchanged variables
Definition of connectors
Definition of component relations
Interface for basic electrical components with two pins (positive and negative)
Generic relations
MODELICA Description
MODELICA

## Slide 20: MODELICA & DYMOLA Overview
Dymola (Short) Overview
Parameters
Variables
Equations
Automatic Component Interface Generation from parameters description
MODELICA

## Slide 21: MODELICA & DYMOLA Overview
Dymola (Short) Overview
Graphical representation described by the MODELICA source code
Modelica source code could be generated graphically
A model could describes the following elements :
Connectors
Parameters
Variables
Sub-components
Equations
Algorithms
…
MODELICA

## Slide 22: MODELICA & DYMOLA Overview
Dymola (Short) Overview
Acausal Description
Determined Causality (automatic)
Determined Causality (automatic)
Component
Executable Model 1
Executable Model 2
MODELICA

## Slide 23: MODELICA & DYMOLA Overview
Dymola (Short) Overview
Modelica Standard Library (« MSL »)
- Version 3.2.2 (Dymola 2017 FD01)
- 1600 Models & Blocs
MODELICA
Standard managed by the MODELICA Association
ABB, AIT, DLR, Dassault Système, Fraunhofer, ITI, Modelon, TU Hamburg-Harburg, Politecnico di Milano, XRG Simulation
MODELICA

## Slide 24: MODELICA & DYMOLA Overview
Dymola (Short) Overview
      Physical or non physical entities description language (continuous, discrete)
      Object oriented
      Mathematical equations and algorithm handling
      Graphical representation management
      Models documentation
      Independent from the solver
      Graphical editor of the MODELICA language for all its aspects
        Icon, Diagram, Documentation and source code MODELICA
      Management of MODELICA source code files and storage
      Models consistency checking (number of equation equal to unknowns)
      Equations manipulation and simplification
      C code generation to build the simulation executable
Dymola
MODELICA
MODELICA
Projet.mo
Code.c
resultat.mat
fmu.dll
dymosim.exe
Dymola
« Generate »
« Generate »
« Compile »
« Compile »
« Interpret »
« Interpret »
« Launch »
« Generate »
« Display »
Visual C++ Express 2010
Language
Editor Compiler Launcher
Process

## Slide 25: MODELICA & DYMOLA Overview
Dymola (Short) Overview
Modeling Interface
Model « views »
Icon, Diagram, Documentation, Modelica
Models Libraries
Hierarchical models list
Icon
Diagram
Documentation
MODELICA source code
Dymola

## Slide 26: MODELICA & DYMOLA Overview
Dymola (Short) Overview
Simulation Interface
Launching Simulations
Parameters, Initial Values, Solvers,…
Results Post-processing
Curves, values, tables, 3D animations
Time evolution
2D Animation
3D Animation
Values
Dymola

## Slide 27: MODELICA & DYMOLA Overview
Dymola (Short) Overview
period = 20 ms
Sub sampled signal
Sampled “System” Control (100 ms)
Electrical Motor
Mechanical Pump
Sampled “Equipment” Control (20 ms)
Multi-physical example of a controlled motorized pump
Based only on Modelica Standard Library components
Using Synchronous capabilities of MODELICA language
Dymola

## Slide 28
Dymola (Short) Training

## Slide 29: Use Case Overview
Design PID Controller for a DC Motor*
Dymola (Short) Training
Requirements
For 1rad/s step reference:
Setting Time < 2s
Overshoot < 5%
Steady-state error < 1%
DC Motor Characteristics
J : moment of inertia of the rotor = 0.01 kg.m^2
b : motor viscous friction constant = 0.1 N.m.s
Ke : electromotive force constant = 0.01 V/rad/s
Kt : motor torque constant = 0.01 N.m/Amp
R : electric resistance = 1 Ohm
L : electric inductance = 0.5 H
Control Characteristics
To be determined !
Design
*Source
“Control Tutorials for Matlab & Simulink”

## Slide 30: Design PID Controller for a DC Motor
Dymola (Short) Training
          Objective : Define the engineering activities supposed to be supported by model & simulation
            Pre-Design, Detailed Design, Test Bench Calibration, …
            Performance, Root Cause, Behavioral analysis, …
          Usage : Define how the model will be used by end-users
            Simulation of single operating points, of an aircraft mission ?
            Integration within other models ? Or Standalone usage ?
            Acceptable Simulation Time, Robustness and Accuracy
          Target : Define the computational hardware
            Desktop Computer ? Real Time Simulator ? High Performance Computers
Define Simulation Intent
Define System Model Perimeter
Build the Model
Simulate the Model
Exchange the Model
Define Model Objective, Usage & Target
Main Idea : “One Objective, One Model”
DC Motor Use Case
Objective
Design PID Controller for Performance Requirements
Usage
One single scenario, standalone, control design compatible
Target
Control Engineer Workstation

## Slide 31: Design PID Controller for a DC Motor
Plant Model
Functional model based on main characteristics related to transient conditions
No need to take into account complex phenomena such starting phases (dry friction)
Control Model
- Continuous or sampled PID
Dymola (Short) Training
Define Simulation Intent
Define System Model Perimeter
Build the Model
Simulate the Model
Exchange the Model
DC Motor Use Case
Objective
Design PID Controller for Performance Requirements
Usage
One single scenario, standalone, control design compatible
Target
Control Engineer Workstation
Simulation Mean Requirements
Modeling capability to represent multi-physical plant and control (discrete) modelling
Level of details focused on dynamic behavior
Quick calculation to support control design
No real time constraints
Simulation Mean Choices

## Slide 32: Design PID Controller for a DC Motor
Dymola (Short) Training
DC Motor Use Case
Interfaces
Plant : Electrical pins and speed sensor
Control : Speed Sensor, Command and control target
Architecture
Control + Plant architecture provided for the study
Functionalities
Normal operations only
          Interfaces : Define the system external interfaces
            Physical Interfaces, Signal Interfaces, …
            Characteristics of interfaces linked with the simulation intent.
          Architecture : Define the environment & internal system architecture
            Architecture Breakdown (system, sub-system, assemblies, equipment),
            Elements Connections,
          Functionalities : Define implemented functionalities
            Control laws, system protections,
            Re-configuration
Define the Model Interfaces, Architecture & Functionalities
Define Simulation Intent
Define System Model Perimeter
Build the Model
Simulate the Model
Exchange the Model
Main Idea : “A model represents sub-parts of actual system definition”

## Slide 33: Design PID Controller for a DC Motor
Dymola (Short) Training
DC Motor Use Case
Interfaces
Plant : Electrical pins and mechanical flange
Control : Speed Sensor, Command and control target
Architecture
Control + Plant architecture provided for the study
Functionalities
Normal operations only
Define Simulation Intent
Define System Model Perimeter
Build the Model
Simulate the Model
Exchange the Model
Mechanical Flange
Electrical Pin (Positive)
Electrical Pin (Negative)
Actual Speed
Reference Speed

## Slide 34: Design PID Controller for a DC Motor
Sampled Calculation
Dymola (Short) Training
DC Motor Use Case
Multi-physic
          Multi-physic : Use Multi-Physic modeling tool
            Capability to easily combine several physical domains and level of details, …
            Solvers adapted to solve stiff physical problems.
          Sampled Calculation : Use modeling tool enabling the definition of different sampling time
            Capability to model sampling effect on control properties (stability, robustness, performance…)
            Elements Connections,
          Standards : Use modeling tool based on industry standard (or ongoing ones)
            MODELICA [DYMOLA], VHDL-AMS, Simulink (for control only) …
Build the Model using Adapted Modeling Environment
Define Simulation Intent
Define System Model Perimeter
Build the Model
Simulate the Model
Exchange the Model
Main Idea : “Use Adapted Modeling Tools and Languages”
Dymola
Simulink
Dymola
Standards
Simulink
Dymola

## Slide 35: Design PID Controller for a DC Motor
Dymola (Short) Training
Build the DC Motor Model
Define Simulation Intent
Define System Model Perimeter
Build the Model
Simulate the Model
Exchange the Model
DC Motor Characteristics
J : moment of inertia of the rotor = 0.01 kg.m^2
b : motor viscous friction constant = 0.1 N.m.s
Ke : electromotive force constant = 0.01 V/rad/s
Kt : motor torque constant = 0.01 N.m/Amp
R : electric resistance = 1 Ohm
L : electric inductance = 0.5 H
Dymola
DCMotorSpeed/MotorDrive/Models

## Slide 36: Design PID Controller for a DC Motor
Dymola (Short) Training
Build the Motor Drive Model
Define Simulation Intent
Define System Model Perimeter
Build the Model
Simulate the Model
Exchange the Model
Motor Drive Baseline Definition
Kp : 1 “Proportional Gain”
Ki : 1 “Integrator Gain”
Kd : 1 “Derivative Gain”
Nd : 100 “Numerical Derivative Approximation Parameter ”
Dymola
DCMotorSpeed/MotorDrive/Models

## Slide 37: Design PID Controller for a DC Motor
Dymola (Short) Training
Build the DC Motor Test Case
Define Simulation Intent
Define System Model Perimeter
Build the Model
Simulate the Model
Exchange the Model
Requirements
For 1rad/s step reference:
Setting Time < 2s
Overshoot < 5%
Steady-state error < 1%
Dymola
DCMotorSpeed/MotorDrive/exe

## Slide 38: Design PID Controller for a DC Motor
Validate
Check unit test results
Dymola (Short) Training
DC Motor Use Case
Test
DC Motor Unit Test
Motor Drive Unit Test
DC Motor Design Case
Use
Perform Control tuning
Determine DC Motor State Space Representation
          Test : Perform tests using a bottom-up approach
            Test & Validate equipment, then assemblies, then sub-systems models, …
            Easy debugging of models.
          Validate: Define reference scenarios to validate model behavior
            Use several scenarios that activate all the available functionalities,
            Assess robustness, computational time and accuracy,
          Use: Publish the model
            Document the model definition & limitations,
            Tag the model in a configuration management system for traceability,
            Enjoy your model !
Define Simulation Intent
Define System Model Perimeter
Build the Model
Simulate the Model
Exchange the Model
Main Idea : “Simple to Complex”
Test, Validate and Use the model

## Slide 39: Design PID Controller for a DC Motor
Dymola (Short) Training
Define Simulation Intent
Define System Model Perimeter
Build the Model
Simulate the Model
Exchange the Model
DC Motor Unit Test
Dymola

## Slide 40: Design PID Controller for a DC Motor
Dymola (Short) Training
Define Simulation Intent
Define System Model Perimeter
Build the Model
Simulate the Model
Exchange the Model
Motor Drive Unit Test
Dymola

## Slide 41: Design PID Controller for a DC Motor
Dymola (Short) Training
Define Simulation Intent
Define System Model Perimeter
Build the Model
Simulate the Model
Exchange the Model
DC Motor Design Case
Dymola
Requirements
For 1rad/s step reference:
Setting Time < 2s
Overshoot < 5%
Steady-state error < 1%
Motor Drive Baseline Definition
Kp : 1 “Proportional Gain”
Ki : 1 “Integrator Gain”
Kd : 1 “Derivative Gain”
Nd : 100 “Numerical Derivative Approximation Parameter ”

## Slide 42: Design PID Controller for a DC Motor
Dymola (Short) Training
Define Simulation Intent
Define System Model Perimeter
Build the Model
Simulate the Model
Exchange the Model
Perform Control Tuning
Dymola
Requirements
For 1rad/s step reference:
Setting Time < 2s
Overshoot < 5%
Steady-state error < 1%
Motor Drive Tuned Definition
Kp : ?? “Proportional Gain”
Ki : ?? “Integrator Gain”
Kd : ?? “Derivative Gain”
Nd : 100 “Numerical Derivative Approximation Parameter ”

## Slide 43: Design PID Controller for a DC Motor
Dymola (Short) Training
Define Simulation Intent
Define System Model Perimeter
Build the Model
Simulate the Model
Exchange the Model
Determine DC Motor State Space Representation
Dymola

## Slide 44: Design PID Controller for a DC Motor
Dymola (Short) Training
DC Motor Use Case
Exchange & Integrate Models
Export DC Motor Model to FMU
Import FMU in Simulink
Compare FMU vs Simulink results on DC Motor
Validate control design
          Exchange: Share model with your internal or external customers
            Capitalize the modeling effort, Enables Collaborative Design,
            Requirement for most system developments (Deliverables)
          Integrate: Request for models outside the system perimeter
            Minimize modeling effort,
            Reduce modeling error (elements modeled by the owner of the perimeter),
          Standards: Use standard exchange format
            Simulink : S-Function (but only supported by Simulink)
            Functional Mock-Up Interface (supported by more than 30 tools)
            Scrambled Source Code (C code for instance)
Define Simulation Intent
Define System Model Perimeter
Build the Model
Simulate the Model
Exchange the Model
Main Idea : “Model your system and integrate others models”
Exchange & Integrate Models

## Slide 45: Design PID Controller for a DC Motor
Dymola (Short) Training
Define Simulation Intent
Define System Model Perimeter
Build the Model
Simulate the Model
Exchange the Model
Exchange & Integrate Models
Dymola
Simulink
Simulink
Dymola

## Slide 46
System Simulation at Liebherr

## Slide 47: LTS System Simulation Platform
System Simulation Platform
  Based on standards (Modelica, Simulink,…)
  Enabling interoperability between tools (FMI, C-code,…)
  Addressing the whole development cycle
Multi-domain Strategy
  Enabling models interoperability (control, electrical, thermal, thermodynamic performance,…)
Transverse Capabilities
System Simulation at Liebherr
Simulation
Platform
Valves
Design
Thermodynamic
Analysis
Power
Electronics
Analysis
Thermal
Analysis
Control Design
Mechatronics
Analysis
Architecture
Pre-Design
Fault / Degradation
Analysis
Requirements
Checking
Hardware In
The Loop Verification
LTSThermalLib
Simulink
LTSElectricalLib
LTSMecatronicLib
LTSValveLib
LTSPerformancesLib
LTSPreDesignLib
LTSRequirementsLib
LTSInterfaceLib
Equipment
System
Transverse
LTSAircraftLib
CAT Simulation

## Slide 48: Use Cases
System Simulation at Liebherr
Define Cooling/Heating Requirements (Flow Schedule)
Architecture Definition
Performance Assessment
Control Design
Computer Verification
A/C Integration
Define the performance compliance of system design over the Aircraft flight envelope
Define Physical Architecture & Allocate Performances
Define Control Laws to fulfill transient performances
Verify the compliance of software implementation versus its specification
Verify system integration into the aircraft

## Slide 49: Use Cases
System Simulation at Liebherr
Heat Loads
Flow Schedule
Architecture Definition
Performance Assessment
Control Design
Computer Verification
A/C Integration
Define Cooling/Heating Requirements (Flow Schedule)
Main Inputs : Customer & Regulation Requirements

## Slide 50: Use Cases
System Simulation at Liebherr
Recirculation
Mass Flow Rates
Heat Loads
Architecture Definition
Performance Assessment
Control Design
Computer Verification
A/C Integration
Moist Air
Multi Zones
Cooling
Heating
Water Cont.
Sim. Time : <5s
Dymola
Non-Linear Solver

## Slide 51: Use Cases
System Simulation at Liebherr
Equipment Performance
Architecture Definition
Performance Assessment
Control Design
Computer Verification
A/C Integration
Define Physical Architecture & Allocate Performances requirement on design cases
System Performance
Mass Flow Rate
Temperature
Water Content
Pressure
Main Inputs : Flow Schedule, Architecture Baseline

## Slide 52: Use Cases
Simulation at LTS
Inverse Computation
ACM Performance
Diameters
Rotating Speed
Pressure Ratio
Efficiency
Architecture Definition
Performance Assessment
Control Design
Computer Verification
A/C Integration
Fixed Pressure & Temperature
Fixed Mass Flow, Pressure & Temperature
Fixed Mass Flow, Pressure & Temperature
Fixed Pressure
HX Performance
Wet Efficiency
Pressure Losses
Water Extractor Performance
Efficiency
Pressure Losses
Modular Model
Sim. Time : <1s
Non-Linear Solver

## Slide 53: Use Cases
Simulation at LTS
Define the performance compliance of system design over the Aircraft flight envelope
Architecture Definition
Performance Assessment
Control Design
Computer Verification
A/C Integration
Main Inputs : Frozen Architecture, Equipment Performances Maps
BAS 1
BAS 2
PACK 2
PACK 1
Distribution
Detailed System Performance
Performance Report
Corner Cases
Specification Compliance for Thermodynamic Performance
Control logics validation

## Slide 54: Use Cases
Simulation at LTS
Architecture Definition
Performance Assessment
Control Design
Computer Verification
A/C Integration
IAMS – Cyber Physical Model
Computer
Performance Report
Operating Points for Main components
Performance Margin
Preliminary Control Strategy Validation

## Slide 55: Use Cases
Simulation at LTS

## Slide 56: Use Cases
Simulation at LTS
Specification of Control Algorithm
Specification Compliance for Dynamic Performance
Architecture Definition
Performance Assessment
Control Design
Computer Verification
A/C Integration
Define Control Laws to fulfill transient performances
Main Inputs : Equipment Identification or Model, Control Strategy
Computer
Physical Hardware
Sensors
Commands
Configuration

## Slide 57: Use Cases
Simulation at LTS
Specification of Control Algorithm
Specification Compliance for Dynamic Performance
Architecture Definition
Performance Assessment
Control Design
Computer Verification
A/C Integration
Define Control Laws to fulfill transient performances
Main Inputs : Equipment Identification or Model, Control Strategy
Computer
Physical Hardware
Sensors
Commands
Configuration
Control Model
Dymola
Physical Model

## Slide 58: Use Cases
Simulation at LTS
Architecture Definition
Performance Assessment
Control Design
Computer Verification
A/C Integration
Computer
Control Model
Limited Over/Undershoots
Control Robustness
Control Specification
Control Stability

## Slide 59: Use Cases
Simulation at LTS
Architecture Definition
Performance Assessment
Control Design
Computer Verification
A/C Integration
Rapid Control Prototyping (RCP)
Validation of Control Architecture on Real Physical Hardware
Main Inputs : Control Model, Physical Hardware
RCP Computer
Physical Hardware
Sensors
Commands
Configuration
Control Model
Specification of Control Algorithm
Specification Compliance for Dynamic Performance
C code

## Slide 60: Use Cases
Simulation at LTS
Architecture Definition
Performance Assessment
Control Design
Computer Verification
A/C Integration
Verify the Compliance of Software Design versus its Specification
Main Inputs : Control Law Specification, Software Specification
Computer
Real actuators (Hardware)
Sensors
Commands
Configuration
Computer Model
Physical Model
Verify Compliance of Software Design
Early verification of software Design (Scade Virtual System)

## Slide 61: Use Cases
Simulation at LTS
Architecture Definition
Performance Assessment
Control Design
Computer Verification
A/C Integration
Verify the Compliance of Software Implementation versus its Specification
Computer
Certified C Code Generator
Implementation :
Control laws,
Monitoring,
Logics
Low level Drivers
Main Inputs : Control Law Specification, Software Specification, Electronic Cards
Verify Compliance of Software Implementation

## Slide 62: Use Cases
Simulation at LTS
Architecture Definition
Performance Assessment
Control Design
Computer Verification
A/C Integration
Physical Model
Hardware Controller
Synoptic
Hardware Actuators
Real Time Simulator
Hardware In the Loop Simulation (HiL)
Mature Software Implementation Ready for system test benches

## Slide 63: Use Cases
Simulation at LTS
Architecture Definition
Performance Assessment
Control Design
Computer Verification
A/C Integration
Verify system integration into the aircraft
System
Models
Aircraft Network Simulation
Validation of System integration within the A/C environment (Customer Tests Benches : iron bird, Cabin 0,…)
System Integration Test Benches

## Slide 64
Future of System Simulation

## Slide 65: Toward a Model Based World !
Future of System Simulation
MB Engineering
Design Definition
Geometry, Material, Data,
Life Cycle
MBD
System Definition
Specification, Architecture,
Functions, Interfaces (Models)
MBSE
Analysis
Stress, CFD, Performances,…
Dymola
MBA
Manufacturing
Product Manufacturing
Information, …
MBM
Consider the whole enterprise inlcuding Design, Manufacturing, Factory Design and Services
General trend for Aeronautic and other Industries

## Slide 66: Understanding MBSE
Design Definition
Drawings (Documents)
Future of System Simulation
Before defining MBSE, lets have a look on the product design definition story !
Product Design Definition – Before
  Document Based Approach (“D”)
    Products defined by several drawings,
    Need to synchronize all drawings together in case of change,
    Difficulties to have a global product view,
    Difficulties to exchange with customer (check product physical integration),
    Requires to rebuild information to preform analysis (CFD, FEM,…),
D
Analysis – Stress Calculation
Analysis - Fluid Dynamics
Analysis – Model Based Analysis
MBA
REBUILD Geometry
REBUILD Geometry

## Slide 67: Understanding MBSE
Design Definition
DMU (Model)
Future of System Simulation
Introduction of modeling for drawings using CATIA
Product Design Definition - Currently
  Model Based Approach (“MBD”)
    Products defined uniquely and centralized,
    Generation of drawings enforcing their mutual coherence,
    Enable to have a global product view,
    Support Virtual Integration of the product within the Customer environment,
    Enable to consume design definition for analysis,
MBD
Analysis – Stress Calculation
Analysis - Fluid Dynamics
Analysis – Model Based Analysis
MBA
USE Geometry
USE Geometry

## Slide 68: Understanding MBSE
System Definition
Specification, Architecture,
Functions, Interfaces (Textual)
Future of System Simulation
Analysis – System Performances
Analysis – Computer Validation
System definition similar of having several drawings to define the information
System Design Definition – Currently
  Textual Based Approach (“SE”)
    System definition based on document / textual form (specifications,…),
    Need to synchronize several specifications (software, requirements, interfaces, …) in case of change,
    Difficulties to have a global system view due to increasing complexity, to assess impact analysis, system compliance.
    Difficulties to exchange in an unambiguous way with customers,
    Requires to rebuild system definition for analysis
REBUILD Architecture
Dymola
Analysis – System Regulation
REBUILD Architecture
REBUILD Architecture
SE
MBA

## Slide 69: Understanding MBSE
System Definition
Specification, Architecture,
Functions, Interfaces (Models)
Future of System Simulation
MBSE approach similar to the introduction of CATIA for product definition
System Design Definition – Future
  Model Based Approach (“MBSE”)
    System defined uniquely and centralized,
    Generation of documents enforcing their mutual coherence,
    Enable to have a global product view,
    Support integration of the product within the customer environment,
    Enable to consume design definition for analysis,
System Definition – Model Based System Engineering
MBSE
Analysis – System Performances
Analysis – Computer Validation
Dymola
Analysis – System Regulation
MBA
USE Architecture
USE Architecture
USE Architecture

## Slide 70: MBSE Vision
Future of System Simulation
System Definition
Specification, Architecture,
Functions, Interfaces (Models)
MBSE
Analysis
Stress, CFD, Performances,…
Dymola
MBA
Design Definition
Geometry, Material, Data,
Life Cycle
MBD
Architecture,
Functions,
Interfaces,
Scenarios
Geometry,
Material, Performance Data,..
System Design Justification
Design Justification
Simulink
Dymola
SCADE

## Slide 71
Fluid Modelling & Humidity Effect

## Slide 72: Conservation Equations
Dry Air – Perfect Gas
  State Equation
  Specific Heat
  Enthalpy
Conservation Equations
  Mass Conservation
  Energy Conservation
Fluid Component : 1 Input / 1 Output Case
    Mass Conservation
    Energy Conservation
Fluid Modelling & Humidity Effect
A
B

## Slide 73: Conservation Equations
Practice – Dry Heat Exchange
  Build the following model (Dry_HeatExchange)
Fluid Modelling & Humidity Effect
Q1 - Calculate required “Q_flow” to ensure 10°C temperature variation on the ducts

## Slide 74: Conservation Equations
Fluid Component : 2 Inputs / 2 Outputs Case
    Mass Conservation
    Energy Conservation
Practice – Mixing
Fluid Modelling & Humidity Effect
A
B
C
D
Q1 - Explain observed temperature variations
Q2 - What is the fundamental relation between temperature and fluid flow ?

## Slide 75: Moist Air Modelling
  Moist Air
    Moist Air State Variable
    Mass Fractions w.r.t Moist Air Mass
    Mass Fractions w.r.t. Dry Air Mass
Mass Conservation Equation
Vapor Water Content
if not saturated :
if saturated :
and if (liquid)
or if
Wet Enthalpy (simplified model)
Where J/kg/K, J/kg and J/kg
Fluid Modelling & Humidity Effect
Mixture Pressure | Mixture Temperature | Mass Fractions
Pa | K | kg/kg of moist air
Mixture Pressure | Mixture Temperature | Mass Fractions
Pa | K | kg/kg of moist air

## Slide 76: Moist Air Impact
Practice – Wet Heat Exchange
  Build the following model (Wet_HeatExchange)
Fluid Modelling & Humidity Effect
Q1 – Explain observed differences w.r.t. dry air case

## Slide 77: Cold Power
  Cabin Dry Cold Power
  Equations
Practice – Dry Cold Power
Fluid Modelling & Humidity Effect
Q1 – Calculate T_F value to obtain T_Cabin=24°C.
Q2 – Validate your calculation by using the model

## Slide 78: Cold Power
  Cabin Wet Cold Power
  Equations
Practice – Wet Cold Power
Fluid Modelling & Humidity Effect
Q1 – Explain observed evolutions

## Slide 79: Cold Power
  Cabin Wet Cold Power
  Equations
Exercice – Dry Air Rated Temperature
    Q1 – Apply conservation equations and derive the following relation:
    Q2 – From the previous relation, determine the definition using the following equation:
Fluid Modelling & Humidity Effect

## Slide 80
Flow Schedule Use Case

## Slide 81: Heat Loads Assessment
Heat Loads Budget in different Aircraft zones
Flow Schedule Use Case
  Metabolic Loads
    Occupants Number (crew member + passengers)
    1 PAX  70W + 1g/min of water produced at 24°C
    1 Working crew member  140W + 2.5g/min of water produced at 24°C
    Taking into account produced water as a load only in case of recirculation
  Electrical Heat Loads
    Lights
    Services Areas
    Avionic bays
    In Flight Entertainment (videos,…)
    For quick pre-design, consider : Pelec = 800 W + 60W / pax
  Solar Loads
    Efficient Windows Area = 0.5 x Total Windows Area (sun light only on one side of the aircraft !)
    Windows Transmissivity : ~0.7
    Solar Heat Flux :1135 W/m2 on ground for clear weather

## Slide 82: Heat Loads Assessment
L
D
External Loads : Conduction and Convection
    Heat Exchange coefficient between Aircraft skin and Cabin Air (internal convection + conduction)
    Total area estimated based on the fuselage diameter (D) and Pressurized Area Lenght (L)
    Skin temperature
      Ground Hot Day Tp (°C) = 1.2368 x OAT (°C)
      Ground Cold Day Tp = OAT
      Flight Tp(K) = OAT (K) x (1+0.18M²)
Flow Schedule Use Case
UA = global Aircraft conductivity (W/K)
Type | U [W/m2/K]
Helicopter / Military Aircraft | 5
General Aviation | 2.4
Business Jet | 1.5
Regional Jet | 1
Single Aisle & Long Range | 0.7

## Slide 83: Cabin Zone Model
    Heat Loads included
                Electrical Power
                IFE Power
                Solar Heat Flux
                Metabolic Power
                External Convective Power
Flow Schedule Use Case
  Heat Loads Model
    Metabolic Power
    External Convective Power
    Skin Temperature

## Slide 84: Cabin Zone Model
Open « CabinMission_PID » Model
Launch simulation
Flow Schedule Use Case

## Slide 85: Cabin Zone Model
Practice – Cabin Zone Model
Plot heat loads evolution (total and particular)
Q1 – In which configuration you observe maximum heat loads ? Explain why.
Q2 – Which conditions enables ECS design for cooling case ? Express these conditions in terme of Aircraft configuration and mission.
Q3 – Which conditions enables ECS design for heating case ? Express these conditions in terme of Aircraft configuration and mission.
Flow Schedule Use Case

## Slide 86: Cabin Zone Model
Flow Schedule Use Case

## Slide 87: Flow Schedule Assessment
Flow Schedule Use Case
3 Cabin Zones
Recirculation

## Slide 88: Flow Schedule Assessment
Thermal Comfort Mass Rate
  Blown temperature limits into cabin
    Without passengers : ~3°C minimum, ~70°C maximum,
    With passengers : between ~8°C and ~50°C.
  Blown liquid water limit into cabin
    1 to 2 g/kg of liquid water maximum.
Pressurization Mass Flow Rate
  Pressurization mass flow rate estimated based on an equivalent aircraft leak area :
    End of life Aircraft leak area generally provided by the aircraft manufacturer,
    Outflow Valve minimum area (minimum regulation position). For pre-design, a rought estimation would consider half of the end-of-life aircraft leak,
    Off-takes coming from power electronics cooling valves.
Fresh Air (O2)
  Fresh flow determined by the number of occupants
    Passengers
    Crew (including pilots)
Flow Schedule Use Case
Normal Mode | Failure Mode
0.55 lb/min/pax | 0.40 lb/min/pax
10 cfm/min
10 cfm/min

## Slide 89: Flow Schedule Assessment
Flow Schedule Use Case
Air System Bleeding on Engine for :
Fresh flow, Heating, Cooling, Pressurization
Low recirculation
Air System Bleeding on Engine for :
Fresh flow, Heating, Pressurization
Refrigerant Cycle
Cooling
Support for High Level Architecture Decisions

## Slide 90
Flow Schedule Practice !

## Slide 91: Flow Schedule Model
Flow Schedule Practice !

## Slide 92: Aircraft Data
Flow Schedule Practice !
Customer Requirements
Aircraft Characteristics
Passengers Number
Mission
Regulation
Enter your values for each zone
Choose your Aircraft
Collect A/C Characteristics,
Estimate passengers & configurations

## Slide 93: Parameters Calibration
Flow Schedule Practice !
  Flow Split setting between zones
    Starting with no recirculation (RECIRC = 0)
    Change flow split to reach 24°C in all zones on ground only
  Recirculation setting
    Technology limitation : Maximum Blown TDAR = -20°C

## Slide 94: Results Visualization
Flow Schedule Practice !
Using provided script to ease results post-treatment

## Slide 95: Design Proposal
Flow Schedule Practice !
Flow Schedule Proposal
  Affine function w.r.t the altitude
    Require margin of 10% (i.e. the gap between the maximum heat load at each altitude shall be majored by 10%)
    Provide function equation !
Flow Schedule Proposal

## Slide 96
Thank you for your attention !